'*************************************************************************

'CWDI Example -- DIGITAL BUFFERED ACQUISITION

'

'Board: Lab-PC-1200

'

'The following connections must be made:

'Digital signal  ---- to Ports A or B (C reserved for handshaking)

'Handshaking pulse train  ---- to PC4 (latches in the data)

'You MUST have a pulse train going in to PC4 or no data will be latched.

'

'In the CWDI Property page, Channel String = 0 for Port A, 1 for Port B

'

Private Sub cmdQuit_Click()

End

End Sub

Private Sub cmdStart_Click()

'START ACQUISITION

CWDI1.Configure

CWDI1.Start

End Sub

Private Sub CWDI1_AcquiredData(Waveform As Variant)

'PLOT DATA

CWGraph1.PlotY Waveform

End Sub