MAGMA and NI Source Cards

The inputs work fine when you go with the defaults, but with the output, you need to adjust the MAGMA drivers so that it is viewed differently in the Windows XP Device Manager.

- Right click on My Computer and Choose Properties.

- Click on Device Manager

- In the Device Manager you will see System devices. In that list you will normally see the MAGMA Box listed as DEC 21152 PCI bridge

- Right click on the DEC21150 PCI bridge and choose properties and then choose the Driver tab.

- Choose Update Driver…

- From Select No, not this time and click Next

- Choose Install from a list or specific location and click Next

- Select Don’t search, I will choose the drive to install

- Choose PCI standard PCI-to-PCI bridge.

- Click Next and install the defaults. After two more reboots the drivers should function properly and the output should work.